## Slide 1: Myo Armband
By Thalmic
https://www.youtube.com/watch?v=te1RBQQlHz4

## Slide 2: The Hardware

## Slide 3: What is it
Sensors
  Medical Grade Stainless Steel EMG sensors
  Highly sensitive nine-axis IMU containing
    three-axis gyroscope
    three-axis accelerometer
    three-axis magnetometer
Communicates by Bluetooth 4.0 low energy
Compatible with most devices, some limitations on OS
Full Details here
  https://www.myo.com/techspecs

## Slide 4: Developers View
Two types of data
  Spatial and Gestural
Spatial Data
  Orientation and movement of the user’s arm
  Two kinds of spatial data
    Orientation – which way is the Myo pointed?
      Provided as a quaternion that can be converted to other representations like rotation matrix or Euler angles (yikes)
    Acceleration vector – acceleration the Myo is undergoing at any given time
      Provided as a 3D vector

## Slide 5: Developers View
Gestural Data
  What is the use doing with their hands
  One of several preset poses (configurations)
Information about which arm and orientation
  Determined with the Sync gesture at start
  Positive X-axis facing either wrist or elbow

## Slide 6: Developers View
Feedback
  Using vibration command
  Causes armband to vibrate in a what that is audible and sensed through touch
Bluetooth driver comes with SDK
Need to install Myo Connect for set up and testing of the Myo
  https://developer.thalmic.com/downloads
  SDK available for Windoiws, MAC and Android
  Includes support for Unity
Built-in capabilities to control certain presentation and media applications on Windows and Mac OS X
  Powerpoint, prezi
  Guide available
Try them out, see how they work